## Slide 1: Design and Development of LLC Resonant Converter for EV charging
( MTP - Stage 1 )
Aditya Kumar
Guide: Prof. Siddavatam Ravi Prakash Reddy
Electrical Machines & Power Electronic Systems (EMPES) Lab
Department of Energy Science and Engineering
Indian Institute of Technology Bombay

## Slide 2: Objective
Theoretical Part
FHA Analysis
Voltage Gain Curves
Hardware Part
Transformer Characterization
Series Resonant Converter (SRC)
LLC Resonant Converter
Operating Modes
Design Parameters

## Slide 3: LLC Converter Specifications
Parameter | Value
Input voltage (Vin) | 60 V
Output voltage (Vout) | 6 V
Resonant tank Inductance (Lr) | 800 µH
Resonant tank capacitor (Cr) | 90 nF
Magnetising Inductance (Lm) of T/F | 3.78 mH
Resonant frequency (fr) | 18 kHz
Output capacitor (C) | 430 µF
Switches and Diodes | Ideal

## Slide 4: LLC Resonant Converter
Equivalent circuit
Equivalent resistance
Resonant frequency
Pole frequency
Voltage gain (FHA)
= =
where-

## Slide 5: Gain vs. switching frequency curve
Light load
(R = 100Ω)
Heavy load
(R = 0.1Ω)
@ Ln = 4

## Slide 6: Key Observations and Inferences
For fs = fr
Gain = 1 (for all Q)
            For fs > fr
            Gain < 1
Can act as Buck or Boost converter
Loading independent operation at fr
Peak doesn’t necessarily occur at fr
Even at no load, output voltage can be regulated easily. (drawback of SRC)
What if the tank parameters are changed
SRC:-
G = =

## Slide 7: Variation in Resonant Tank Parameters
As increases – Gain decreases (less)
As increases – Gain decreases (much)
& ∆f increases
So, we can say that both and ratios
should be low enough.
If we reduce for wide voltage regulation - increases – Poor η
So, trade-off b/w η and voltage regn range
Cr = 10 nF
Lr = 150 µH
Lm = 250 µH
Cr = 22 nF
Lr = 60 µH
Lm = 250 µH
Cr = 10 nF
Lr = 60 µH
Lm = 250 µH
Cr = 22 nF
Lr = 150 µH
Lm = 250 µH
∆f
Notes: Gain reduction – So voltage regulation range is reduced. (we don’t want)
Del f increases – So operational frequency variation increases. (we don’t want)
1  0.145 fo = 7.25 kHz and
3  0.247 fo = 12.35 kHz (for fo = 50 kHz)

## Slide 8: Key Observations
As increases – Gain decreases (less)
As increases – Gain decreases (much)
& ∆f increases
So, we can say that both and ratios
should be low enough.
If we reduce for wide voltage regulation - increases – Poor η
So, trade-off b/w η and voltage regn range
∆f
Notes: Gain reduction – So voltage regulation range is reduced. (we don’t want) Del f increases – So operational frequency variation increases. (we don’t want)

## Slide 9: Behaviour of the LLC Voltage-Gain
Control variable - fn
Normalized frequency corresponding to resonant peak () is moving w.r.t. change in load (and thus w.r.t. change in Qe)
Irrespective of combn of Qe and Ln, (Mg, fn) = (1, 1) for all curves (irrespective of the loading conditions)
For a fixed Ln, if Qe  shrinks the curve,
lowers the curve,
shifts towards f0
For a fixed Qe, if Ln  shrinks the curve
shifts towards f0
peak gain increases
Notes: Let’s take an simple illustration,
As RL : Infinite  0
Qe : 0  Infinite
Mg-peak : Infinite  1
fc0 : fp  f0
For a fixed Qe, decrease in Ln shrinks curve, the whole curve is squeezed (horizontally) and fc0 moves
towards f0. Also, peak gain increases and better freq. control band.

## Slide 10: Behaviour of the LLC Voltage-Gain
Control variable - fn
Normalized frequency corresponding to resonant peak () is moving w.r.t. change in load (and thus w.r.t. change in Qe)
Irrespective of combn of Qe and Ln, (Mg, fn) = (1, 1) for all curves (irrespective of the loading conditions)
For a fixed Ln, if Qe  shrinks the curve,
lowers the curve,
shifts towards f0
For a fixed Qe, if Ln  shrinks the curve
shifts towards f0
peak gain increases
Notes: Let’s take an simple illustration,
As RL : Infinite  0
Qe : 0  Infinite
Mg-peak : Infinite  1
fc0 : fp  f0
For a fixed Qe, decrease in Ln shrinks curve, the whole curve is squeezed (horizontally) and fc0 moves
towards f0. Also, peak gain increases and better freq. control band.

## Slide 11: Modes of Operation
At fr
Above fr
Below fr

## Slide 12
Operation at Resonance
When Q1 turns off,
  Ir falls to Im
  So, no power transfer to secondary side.
By delaying Q2 turn on,
  we can achieve primary ZVS,
  Soft commutation of rectifier diodes on secondary side.
Operation Above Resonance
ILr is in CCM
  Less RMS current is required for same energy to load
  Less conduction losses
Still primary ZVS is achieved.
Rectifier diode – Not soft commn
Operation Below Resonance
ILr falls to Im before the end of driving pulse,
  So power transfer is stopped even before even though Im continues.
Still achieve primary ZVS and soft commutation of rectifier diodes.
Diodes – DCM. So, require more circulating current to deliver the same energy to load
which results in more conduction loss
If fsw << f0 : ZVS may be lost

## Slide 13: Design Considerations
Image Source: TI Power supply design seminar, Literature number SLUP263

## Slide 14: Design Steps

## Slide 15: Transformer Characterization (5:1)
Open Circuit Test
LV Energized : Lp = 178.60 µH
Rp = 350 mΩ
HV Energized : Lp = 3.78 mH
Rp = 9.27 mΩ
Short Circuit Test
LV Energized : Ls = 1.08 µH
Rs = 23.01 mΩ
HV Energized : Ls = 24.62 µH
Rs = 1.2 mΩ
Lr = 24.62 µH
Lm = 3.78 mH
(very high)

## Slide 16: Experimental Setup
Specifications
Nova board – used as inverter
IGBTs - IKW25N120H3
Additional Inductor – 775.28 µH, 5A
Capacitor – 481.67 nF, 288 nF (Bipolar)
Electronic Load – 2 Ω
Microcontroller – TMS320F28379D

## Slide 17: Experimental Setup
Specifications
Nova board – used as inverter
IGBTs - IKW25N120H3
Additional Inductor – 775.28 µH, 5A
Capacitor – 481.67 nF, 288 nF (Bipolar)
Electronic Load – 2 Ω
Microcontroller – TMS320F28379D

## Slide 18: DC-DC Series Resonant Inverter (SRC)
VAB, VCD, ILr, VLr
Observations
15 kHz – Discontinuous conduction mode
Highest output voltage doesn’t necessarily occur at fr
Inductor voltage spikes are more at 35 kHz
Irregularity – At 35 kHz, inductor current trend
- At 15 kHz VCD glitches
fsw = 25 kHz
fsw = 15 kHz
fsw = 35 kHz

## Slide 19: DC-DC Series Resonant Inverter (SRC)
VAB, VCD, ILr, VLr
Observations
15 kHz – Discontinuous conduction mode
Highest output voltage doesn’t necessarily occur at fr
Inductor voltage spikes are more at 35 kHz
Irregularity – At 35 kHz, inductor current trend
- At 15 kHz VCD glitches
fsw = 25 kHz
fsw = 15 kHz
fsw = 35 kHz

## Slide 20
VAB, Idc, Vo, Io
DC-DC Series Resonant Inverter (SRC)
fsw = 15 kHz
fsw = 25 kHz
fsw = 35 kHz

## Slide 21: SRC Converter - Experimental Results
fsw = 15 kHz
fsw = 25 kHz
fsw = 35 kHz

## Slide 22: LLC Resonant Converter
VAB, VCD, ILr, VLr
Some Observations
12 kHz – No discontinuous conduction
(No DCM even at low fsw)
At fr and more than fr, results are closely matching
As fsw is increased, VCr is reduced
Irregularity – Simulation is not able to mimic behaviour at low switching frequencies
fsw = 12 kHz
fsw = 18 kHz
fsw = 30 kHz

## Slide 23: LLC Resonant Converter
VAB, VCD, ILr, VLr
Some Observations
12 kHz – No discontinuous conduction
(No DCM even at low fsw)
At fr and more than fr, results are closely matching
As fsw is increased, VCr is reduced
Irregularity – Simulation is not able to mimic behaviour at low switching frequencies
fsw = 12 kHz
fsw = 18 kHz
fsw = 30 kHz

## Slide 24: LLC Resonant Converter
VAB, Idc, Isec, Vo
fsw = 12 kHz
fsw = 18 kHz
fsw = 30 kHz

## Slide 25: LLC Converter - Experimental Results
fsw = 12 kHz
fsw = 18 kHz
fsw = 30 kHz

## Slide 26: Key Takeaways and Conclusion
Based on domain knowledge, some initial guess has to be taken between and selection as a starting point in converter design
Generally, there is a trade-off is observed between η and wide voltage regulation range
Future Work
Moving to 1 kW, 400V – 48V LLC resonant converter hardware and closed loop control

## Slide 27: Thank You

## Slide 28: PRC and LLC Readings
 | At fr | Above fr | Below fr
PRC | 1.52 A | 1.08 A | 2.5 A
LLC | 1.25 A | 0.428 A | 1.402 A
PRC | 0.8 A | 0.474 A | 1.18 A
LLC | 0.22 A | 0.066 A | 0.294 A

## Slide 29: Feedback
Why there is a dip in VCD at 15 kHz in SRC ?
and why it is not at fr or > fr ?
Why ILr is not in DCM in hardware, but its in DCM in simulation ?
Why we are not in DCM even at very low fsw ?